## Slide 1
Guidelines for safe and effective phototherapy

## Slide 2: Guidelines for optimising phototherapy – equipment factors
Use special blue tubes or LED light source
  Using only white tube lights is less effective
Monthly irradiance check with flux meter is a must
  Ideal irradiance of at least 30 microW/cm2/nm
Pic of CFL blue light phototherapy / flux meter

## Slide 3: Guidelines for optimising phototherapy – equipment factors
Keep the phototherapy unit as close as possible [up to 15 cms] ensuring that the neonate maintains normal temperature
Align the phototherapy unit so that the neonate lies directly beneath the centre of the unit
Pic of PT unit placed close to the baby

## Slide 4: Measures to increase effectiveness of phototherapy
Increase the exposed body surface area of the infant under phototherapy
  by placing another phototherapy unit beneath/ by the side of the neonate
  reflecting material around the incubator or radiant warmer bed is optional
  Keep the diapers as short as possible
Pic of double surface PT
Reflecting white cloth around the PT unit not occluding the fan/ reflecting material

## Slide 5: Supportive care
Ensure adequate hydration- Continue breast feeding/ breast milk feeding
No role of routine intravenous fluids or supplemental feeds, unless baby is clinically dehydrated
May interrupt for feeding/ clinical care procedures provided total serum bilirubin is lower than exchange threshold
Monitor urine output

## Slide 6: Supportive care
Cover the eye with opaque eye patches
Monitor temperature every 2 hours
Routine position changing is not recommended
Pic of neonate with eye patch